## Slide 1
Measures to Reduce Noise of Night Operations
Prague Airport

## Slide 2
Aircraft noise: Regulations
  Prague Airport – responsibility for complying with national noise limits
    Act No 258/2000 Coll. on protection of public health
    Act No 49/1997 Coll. on civil aviation
    Regulation (EU) No 598/2014 of the European Parliament and of the Council on the establishment of rules and procedures with regard to the introduction of noise-related operating restrictions at Union airports within a Balanced Approach and repealing Directive 2002/30/EC
    ICAO Doc 9829, Guidance on the Balanced Approach to Aircraft Noise Management.
    National noise limits: daytime - LAeq,16 h = 60 dB, night-time - LAeq, 8 h = 50 dB (outdoor spaces)
    Characteristic air-traffic day: an average air-traffic day in the six-month period with the heaviest air traffic (May to October)

## Slide 3: Balanced Approach to Aircraft Noise Management at LKPR
Noise reduction at the source: Noise charges – significant change starting 03/2018
Landscape planning and management: Noise Protection Zone of Prague/Ruzyně Airport - Noise barrier measures
Anti-noise operational measures:
  RWY system preference.
  Anti-noise procedures for approach/departure.
  Rules for the reduction of reverse thrust.
  Rules for carrying out engine tests.
  Rules for using APUs.
Operational restrictions:
  Restricted access for aircraft without the corresponding certification according to ICAO, Annex 16/I.
  Restricted operation at night: access only for the types and versions of aircraft that are on the Bonus list and meet the criteria for the Airport’s noise policy.
  Limited allowance of 48 coordinated flights during night period – Slot Coordination

## Slide 4: Noise situation at night (22:00 – 06:00)
Noise Protection Zone of Prague Airport + Night noise contours
Noise protection zone
Night limit noise
contour – 50 dB
Continuous monitoring station, Bažantní street, Suchdol – 2017: 50,8 dB
Mobile monitoring station, U Kapličky street, Suchdol – 2017: 53,8 dB

## Slide 5: Results of Air Traffic Noise Monitoring
Noise Monitoring Results: U Kapličky, Suchdol
  Critical situation with number of aircraft MVT during night!
  High possibility of exceeding of noise limit for night.
  A lot of complaints from majors, inhabitants, NGOs.
  HSHMP (Public Health Authority) requires effective action to be taken.
  Potential risk of operating restrictions acc. to Act No 49/1997 Coll. on civil aviation.
Year | Method | Laeq_Day_CHLD [dB] | Laeq_Night_CHLD [dB] | Average MVT | Y/Y increase of MVT
2015 | Mobile monitoring | 57.4 | 51.6 | 45 | 0 %
2016 | Mobile monitoring | 57.4 | 52.0 | 49 | 8.9 %
2017 | Mobile monitoring | 58.6 | 53.8 | 54 | 20 %
2018 | Calculation | 59.1 + 60.7 | 52.9 – 54.5 | 63 | 40 %
Night noise limits: 50 dB ± 2.4 dB
*for period 01.01. - 02.08.2018

## Slide 6: Action plan
Prague Airport processed Action Plan for next 3 years based on Balanced Approach to Noise Management (ICAO Doc 9829, Regulation (EU) No 598/2014, Act No 49/1997 Coll.).
Action Plan and particular measures have been discussed with national authorities:
Civil Aviation Authority
Air Navigation Services
Ministry of Transport
The proposed measures are primarily aimed at ensuring compliance with current valid AIP CR regulations (GEN 1.2.1.8.2 Breach of coordination procedures and GEN 4.1.1.4 Noise charges) and operational measures and restrictions if the previous measure proved to be insufficiently effective.
The steps below will be applied gradually until the noise situation improves.
Effectiveness of the measures requires close cooperation with relevant partners including airlines.

## Slide 7: Action plan
S2019
Efforts to avoid night landings without a coordinated night slot after 23:00 LT
Prevention of earlier departures (flight plan discrepancies with coordinated time) Implementation of the A-CDM milestone 1
Efforts to avoid earlier landings with a daytime slot before 06:00 LT
Proposal for Slot Coordination of the Czech Republic to reduce the number of night slots
Reducing the List of allowed aircraft types for night operations in AIP
Partial night closure – postponed to 2020
All the proposed measures are based on information and data available in August 2018.

## Slide 8: Action plan
S2020
Adjustment of Airport charges (not permitted noise cat.)
Limitation of noise categories permitted for night operation
Further proposal for Slot Coordination of the Czech Republic to reduce the number of night slots
  - Additional condition for calculating historical slots for season S20:
  50% of the flights of series have to be operated plus or minus 30 minutes of the allocated slot
4. Partial night noise closure acc. to Act No 49/1997 Coll. on civil aviation
5. Limitation of cargo flights at night
S2021
Night noise closure acc. to Act No 49/1997 Coll. on civil aviation
Imposed by Civil Aviation Authority
All the proposed measures are based on information and data available in August 2018.

## Slide 9
Thank you for your attention