## HOURLY CAPACITY FIGURES FOR S24 SEASON (PRG/LKPR)

The operation in all airport terminals is fully coordinated for the entire season in accordance with the limitations applied to flights to/from the Schengen states:

Terminal T1 – flights to/from countries outside of the Schengen area

Terminal T2 – flights to/from countries within the Schengen area
Terminal T3 – General and Business Aviation Terminal

PARKING STANDS – Main apron North + East

Total of 49 aircraft stands divided as follows:

  - 1 stand for aircraft with wingspan up to 80m

  - 5 stands for aircraft with wingspan up to 65m

  - 2 stands for aircraft with wingspan up to 52m

  - 1 stand for aircraft with wingspan up to 39m

  - 35 stands for aircraft with wingspan up to 36m  	(-2 stands)

  - 5 stands for aircraft with wingspan up to 29m

GATES

  - T1: 	 22 GATES

  - T2:	 27 GATES 						(-1 gate)

  - T3:	   2 GATES

TERMINALS

Departures

  - T1:	1900 passengers (limiting factor – passport control)

  - T2:	2500 passengers (limiting factor – boarding pass validators)

  - T3:	    70 passengers (limiting factors – gate + security control)

Arrivals

  - T1:	1900 passengers (limiting factor - passport control

  - T2:	3500 passengers (limiting factor – baggage claim)

  - T3:	  120 passengers (limiting factor – baggage claim)

RUNWAYS

Movements from 04:00 to 19:55 UTC

0400 – 1955UTC	  6ARR +   6DEP + 10total/10min

33ARR + 33DEP + 46total/60min

0730 – 0930UTC	                                47total/60min

1400 – 1600UTC	                                47total/60min

Movements from 20:00 to 03:55 UTC – night noise curfew

2000 – 0355UTC	  6ARR + 6DEP + 10total/10min

2000 – 0355UTC	48 movements

0000 – 0155UTC 	  0 DEP

- total number of night airport slots = 8103 in season S24

(the quota of night slots for carriers was determined according to the historical slots of carriers calculated for the S23 season)

- take-offs and landings are permitted solely for the aircraft from Bonus List

- valid only for aircraft falling into noise category 1-9!!

Bonus List - List of Aircraft permitted for night operation (IATA codes)

141, 142, 143, 14X, 14Y, 14Z,

221, 223, 290, 295, 318, 319, 31B, 31N, 320, 32N, 32Q, 321, 32A, 32B,

332, 333, 338, 339, 342, 343, 345, 346, 351, 359, 388

717, 734, 735, 736, 738, 739, 73C, 73E, 73G, 73H, 73J, 73W, 74H, 74N, 752, 753, 75M, 75T, 75W,

762, 763, 764, 76W, 772, 773, 77L, 77W, 781, 788, 789, 7M1, 7M7, 7M8, 7M9, 7S8, 7S9

AB6, AR1, AR7, AR8, ARJ, CC6, CCX, E90, E95, GJ6, S9S, SU7, SU9